Sharjah Indian School – Boys Wing

Answer Key to Vacation assignments -2010 on  Physics    (class 12)

- Find the force on the charge Q placed at the centroid of an equilateral triangle of side ‘a’ with equal

charges q placed on the vertices.  [Ans: 0]

- Two charges 3x10 -8 C and -2 x 10-8 are located 15cmapart. At what point on the line joining the two charges is the electric potential be zero?  [Ans: at 9 cm from 3 x 10 -8C]

- Draw equi-potential surfaces for a uniform electric field pointing along +z axis.

- A parallel plate capacitor is to be designed with a voltage rating lkV using a material of dielectric constant 3 and dielectric strength of 107 V/m. For safety, we would like the field never to exceed say, 10% of the dielectric strength. What minimum area of the plates is required to have a capacitance of 50pF?

[Ans: 19 cm2]

- An electrostatic field line cannot be discontinuous. Why?

- Write the magnitude and direction of electric field intensity due to an electric dipole of length 2a at the mid-point of the line joining the two charges. [Ans: kq/r2 towards –ve charge]

- A 4µF capacitor is charged by a 200 V supply. The supply is then disconnected and the charged capacitor is connected to another uncharged 2 µF capacitor. How much electrostatic energy of the first capacitor is lost in the process of attaining the steady situation? [Ans: 2.67 x 10 -2J]

- How does the resistivity of (i) a conductor and (ii) a semiconductor vary with temperature? Give reason for each case.

- Two fixed point charges + 4 e and + e units are separated by a distance ‘a’. Where should the third point charge be placed for it to be in equilibrium? [Ans: 2/3 a from +4e]

- An electric dipole of dipole moment 20 x 10-6C.m is enclosed by a closed surface. What is the net flux coming out of the surface? [Ans: 0]

- A parallel plate capacitor with air between the plates has a capacitance of 8 pF. What will be the capacitance if the distance between the plates be reduced by half and the space between them is filled with a substance of dielectric constant K = 6?  [Ans: 96 pF]

- Three point charges of +2µC, -3µC and -3 µC are kept at the vertices

A, Band C respectively of an equilateral triangle of side 20 cm

as shown in the figure. What should be the sign and magnitude

of the charge to be placed at the mid-point (M)

of side BC so that the charge at A remains in equilibrium? [ +3.9 µC]

- How can the sensitivity of a potentiometer be increased?  [Ans: By introducing a resistor in series in the primary circuit.]

- A voltage of 30 V is applied across a carbon resistor with first, second and third rings of blue, black and  yellow colours respectively. Find the value of current through the resistor. [Ans: 5 x 10 -5A]

- Two dielectric slabs of dielectric constants K1 and K2

are filled in between the two plates, each of area A

of the parallel plate of a capacitor as shown in the figure.

Find the net capacitance of the capacitor.[ (oA/2d . (K1+K2)

Page 01/04

- A small metal sphere carrying charge +Q is located

at the centre of a spherical cavity in a large un charged

metal sphere as shown in the figure.

Use Gauss' theorem to find electric field at points P1 and P2.

[ Ans: E1 = kQ/r2     and E2 = 0]

- A heating element using nichrome connected to a 230 V supply draws an initial current of 3.2 A which settles after a few seconds at a steady value of 2.8 A What is the steady temperature of the heating element if the room temperature is 27oC. Temperature coefficient of resistance of nichrome averaged    over the temperature range involved is 1.7 x 10-4°C-1     [ Ans: 867oC]

- Two primary cells of e.m.f. EI and E2(EI> E2)are connected

to the potentiometer wire AB as shown in the figure.

The balancing lengths for the two combinations

of the cells are 250cm and 400 cm, find the ratio of E1 andE2.

[ Ans: 13 : 3]

- In a metre bridge, the balance point is found to be at

39.5 cm from the end A, when the resistor Y is of 12.5 ohm.

Determine the resistance of X. Why are the connections

between resistors in a metre bridge made of thick

copper strips? What happens if the galvanometer and cell

are interchanged at the balance point of the bridge? Would the galvanometer show any current?

[Ans: ( a) 8.2Ω  - to minimize the resistance of the circuit.   (b) 60.5cm from A     (c) No ]

- An electron beam projected along + X-axis experiences a force due to the magnetic field along the

+Y-axis. What is the direction of the magnetic field?  [-Z axis]

- A galvanometer with a coil of resistance 120 ohm shows full scale deflection for a current of 2.5 mA How will you convert the galvanometer into an ammeter of range 0 to 7.5 A ? Determine the net resistance of the ammeter. When an ammeter is put in a circuit, does it read slightly less or more than the actual current in the original circuit? Justify your answer.  [Ans: S = 0.04 Ω]

- Two small identical circular loops, marked (l) and (2),

carrying equal currents, are placed with the geometrical

axes perpendicular to each other as shown in the figure.

Find the magnitude and direction of the net magnetic field

produced at the point O.  [ Ans: (2  (µoIa2)/2(a2+x2)3/2   at 45o]

- A charged particle enters into a uniform magnetic

field and experiences an upward force as indicated

in the figure. What is the charge sign on the particle?

[ Ans: positive  (Use Fleming’s L.H.Rule)]

- Figure shows a rectangular current-carrying loop placed 2 cm

away from a long, straight, current carrying conductor.

What is the direction and magnitude of the

net force acting on the loop?

[Ans: 7.82 x 10 -5N repulsion]

Page 02/04

- A short bar magnet of magnetic moment 0.9 joule/ tesla, is placed with its axis at 45o to a uniform magnetic field. If it experiences a torque of 0.063joule, (i) calculate the magnitude of the magnetic field and (ii) what orientation of the bar magnet corresponds to the stable equilibrium in the magnetic field ?       [ Ans: 0.099T	θ = 0]

- A potential difference of V volt is applied across a copper wire of length l and diameter d. How will the drift velocity be affected if-

(i) V is doubled

(ii) l is doubled.    [(i) vd doubles (ii) vd is halved]

- Two cells of same emf E, but different

internal resistance rl and r2 are connected to

an external resistance R as shown. in the figure.

The voltmeter V reads zero. Obtain an expression

for R in terms of rl and r2. Calculate the voltage

across the cell of internal resistance r2. (Assume that the voltmeter V is of infinite resistance).

[ Ans: R = r1 – r2                                  V2 = E(1 – r2/r1)]

- In the figure given below, PQ is a long straight wire carrying a current

of 5A in the direction of the arrow. An electron travels with a velocity

of 106 m/s at a distance 10 cm from the wire in the same direction

of the current. Calculate the magnitude and direction of the force

experienced by the electron.

[ Ans: 1.6 x 10 -18N away from the wire]

P

- A straight wire, of length L, carrying a current I, stays suspended horizontally in mid air in a region where there is a uniform magnetic field B . The linear mass density of the wire is λ. Obtain the magnitude and direction of this magnetic field.

[ Ans: B = (I/g  perpendicular to the plane]

- A charged particle, having a charge q, is moving with a speed v along the x-axis. It enters a region of space 'where an electric field E (= E j) and a magnetic field B are both present. The particle, on emerging from this region, is observed to be moving along the x-axis only. Obtain an expression for the magnitude of B in terms of v and E. Give the direction of B.

[Ans: B = E/v along Z axis]

- Find   (i) the .equivalent capacitance and

(ii) the total energy stored in the system

of capacitors given in the network.

The charging battery has an emf of 4V.

[Ans: 1µF (approx.)    &   8 x 10 -6 J (approx.)

- In the figure shown, calculate the total flux

of the electrostatic field through the spheres S1 and S2 The wire,

AB, shown here,  has a linear charge density, λ  given by λ = kx

where x is the distance measured along the wire, from the end A.

[   Ans: Q/(o       and    ( ½ kl2 + Q )/ (o)

- A cell, of emf 4 V and .internal resistance 0.5 Ω, is connected across a load of resistance (i) 7.5 Ω,

(ii) 11.5 Ω. Calculate (i) the ratio of the differences in the emf of the cell and the potential drop across the

load, and (ii) the ratio of the currents in the two cases   [Ans: (i) 3:2	(ii) 3:2]

- A potentiometer wire has a length L and a

resistance Ro. It is connected to a battery and

a resistance combination as shown.

Obtain an expression for the potential drop

per unit length of this potentiometer wire.

What is the maximum emf of a 'test cell' for which  one can get a 'balance point' on this potentiometer wire ? What precaution should one take, while connecting this 'test cell' , in the circuit?

[Ans: [E/(RS/R+S)] Ro/L                                  Max emf= E/(RS/R+S)] Ro     Connect positive to A]

- A series battery of 10 lead accumulators each of emf 2 V and internal resistance 0.25 ohm is charged by a 220 V D.C. mains to limit the charging current a resistance of 47.5 ohm is used in series in the charging circuit. What is  a) the power supplied by the mains and b) power dissipated as heat? Account for the difference of powers is (a) and (b). [Ans: (a) 880W  (b) 800W    -Stored as  chemical energy in cells]

- A proton moves with a speed of 7.45 x 105 m/s directly towards a free proton originally at rest. Find the distance of the closest approach for the two protons. (Given: mass of proton = 1.67 x 10 –27 kg and e = 1.6 x 10 –19 C)		[Ans:0.41m]

- The electron in the hydrogen atom circles around the proton with a speed of 2.18 x 106 m/s in an orbit of radius 5.13 x 10 -11 m. What magnetic field does it produce at the centre?

[Ans: 13.3 T]

- By applying kirchoff’s laws, calculate the current flowing through each resistance in the network shown in this diagram.

2 V

A	B

4.5 ohm

1V	1 ohm

D	C

1 ohm

[Ans: 0.87A through 1V, 0.35A through 2V and 0.52A through 4.5 Ω]

- Figure shows a bar magnet M falling under gravity

through an air cored coil C. Plot a graph

showing the variation of induced e.m.f (E) with time (t).

What does the area enclosed by the

E - t curve depict ?

[Change in flux]

- Figure (a), (b) and (c) show three a.c. circuits in which equal currents are flowing. If the frequency of emf be increased, how will the current be affected in these circuits? Give reason for your answer.

[ Ans: (a) decreases    (b) no change     (c) increases	Page 04/04